## Slide 1: ECE477 Midterm Design Review: Team 3
<Add team picture or relevant project picture here>

## Slide 2: Outline
Project Overview
Major Components
Block Diagram
Packaging Design
Electrical Schematic
PCB Layout
Prototyping Progress
Software Development Status
Project Timeline
Questions

## Slide 3: Project Overview
NYAKB is a newcomer in the growing mechanical keyboard community that includes a high quality, phone sized LCD screen that will display various information, and can interact with the keyboard itself. The module will be detachable. Current keyboards on the market don't have the unique display functionality NYAKB has.
Not your average Keyboard (NYAKB)

## Slide 4: PSSCs
PSSC #1 (Hardware): An ability to have a key switch matrix for the various typing keys on a keyboard that can be scanned and debounced for clean inputs by the microcontroller on the main keyboard module.
PSSC #2 (Hardware): An ability to drive an LCD display via SPI.
PSSC #3 (Hardware): An ability to step down 5V USB input power to 3.3V for the main keyboard MCU and display module MCU/display.
PSSC #4 (Hardware): An ability to have the main keyboard MCU serve as master and communicate to submodule MCU as slave over I2C.
PSSC #5 (Hardware): An ability to communicate key presses from the user to the Host PC over a USB connection.

## Slide 5: Major Components
Buck Converter: TPS563231DRLT
Specs:
  Input range 4.5V-17V
  Output 3.3V
  Max Current 3A
Usage:
  This will be used to step down USB 5V input to 3.3V that will power the main keyboard (stm32f4) as well as submodules via the hot plug connection
Power Regulation

## Slide 6: Major Components
Voltage Regulator: LD1117S33TR_SOT223
Specs:
  Input (Max) 15V
  Output (Min/Fixed) 3.3V
  Dropout 1.2V @ 800mA
Usage:
  Built into the decoupling capacitor to step down the 5V input from the programming header on the sub-module device to 3.3V
Power Regulation

## Slide 7: Major Components
Voltage Regulator: BAT60JFILM
Specs:
  Schottky Diode
  DC Reverse Vr (Max) 10V
  Forward Vf (Max) 580mV @ 1A
Usage:
  Drop 3.3V to 3V0 for the SPI LCD display
Power Regulation

## Slide 8: Major Components
Main Keyboard MCU: STM32F407VGT6
Specs:
  USB FS Controller
  I2C hardware blocks
  GPIO
Usage:
  This MCU will be used to communicate with the host PC over USB and to submodules over I2C. It will also scan the key matrix using GPIO
Power Consumption:
  Max: 240mA @ 3.3V
Microcontrollers

## Slide 9: Major Components
sub-module MCU: STM32F091RCT6
Specs:
  I2C hardware blocks
  SPI hardware blocks
Usage:
  This MCU will be used to communicate with the SPI TFT LCD display to render info and to the main keyboard over I2C over the hot plug connector.
Power Consumption:
  Max: 120mA @ 3.3V
Microcontrollers

## Slide 10: Major Components
Display: MSP3520
Specs:
  3.5" TFT display module
  320x480px resolution
Usage:
  Controlled over SPI
  Present visual information to user
Power Consumption:
  Approx. 84mA @ 3.0V
Display

## Slide 11: Block Diagram

## Slide 12: Packaging Design
We've opted for a new layout, so we've changed our packaging plans as well.
We'll be sandwiching the PCB between laser cut acrylic plates, and mounting them with screws.
Dimensions:
  365mm x 142mm
Changes to our Packaging

## Slide 13: Packaging Design
Outer layer 295x103x12 mm
Inner layer 286x94x8 mm
3 access points to allow it to connect to other modules, and a point of access to connect to the USB port.
We will be using acrylic to create the packaging
Keyboard design has evolved
Main Keyboard Original Design

## Slide 14: Packaging Design
Outer layer 83x103x12 mm
Inner layer 72x94x8 mm
Access point located on the left side of the device
Opening left for the LCD display to be seen
Plan to match materials with main keyboard by using the same acrylic
Keyboard design has evolved
sub-module Original Design

## Slide 15: Electrical Schematic
Main Keyboard Overview

## Slide 16: Electrical Schematic
Main Keyboard Crystal Oscillator

## Slide 17: Electrical Schematic
Main Keyboard Buck Converter

## Slide 18: Electrical Schematic
Main Keyboard Connectors

## Slide 19: Electrical Schematic
Main Keyboard KeySwitch Matrix

## Slide 20: Electrical Schematic
sub-module overview

## Slide 21: Electrical Schematic
sub-module programming header

## Slide 22: Electrical Schematic
sub-module Decoupling capacitors

## Slide 23: Electrical Schematic
sub-module Connectors

## Slide 24: Electrical Schematic
sub-module Reset and Pull down

## Slide 25: Electrical Schematic
sub-module Testing

## Slide 26: PCB Layout
Main Keyboard Overview

## Slide 27: PCB Layout
Main Keyboard Microcontroller

## Slide 28: PCB Layout
Main Keyboard Crystal Oscillator

## Slide 29: PCB Layout
Main Keyboard Buck Converter

## Slide 30: PCB Layout
Main Keyboard USB

## Slide 31: PCB Layout
Main Keyboard Hot PLUG and Debug

## Slide 32: PCB Layout
Main Keyboard BOOT0 Switch

## Slide 33: PCB Layout
Main Keyboard KeySwitch

## Slide 34: PCB Layout
sub-module Design overview

## Slide 35: PCB Layout
sub-module Microcontroller

## Slide 36: PCB Layout
sub-module Programming Header

## Slide 37: PCB Layout
sub-module Programming Header Decoupling

## Slide 38: PCB Layout
sub-module Decoupling Capacitors

## Slide 39: PCB Layout
sub-module Reset and pull down

## Slide 40: PCB Layout
sub-module Connectors

## Slide 41: PCB Layout
sub-module Testing Connectors

## Slide 42: PCB Verification
sub-module Front

## Slide 43: PCB Verification
sub-module Back

## Slide 44: Prototyping Progress
Prototyped buck converter made from discrete components
  Opted to buy IC buck converter for use in our voltage regulator
Bi-directional communication between micro-controllers tested and proven functional
SPI display tested and proven functional
Key matrix scanning tested, need to verify that scaling to larger key counts
Implementing one possible software method of key debouncing
USB FS controller known to be capable of enumerating as HID
  Need to test power draw capabilities

## Slide 45: Software Development Status
Task priority scheduling (In progress)
I2C module communication
  Simple single byte bi-directional messages (Completed)
  Multi-byte messages (In development)
Common software functionality

## Slide 46: Software Development Status
Keyboard Scanning (In development)
  Have smaller keypad without anti-ghosting diodes for prototyping, need to scale up to full key matrix upon PCB assembly
Key debouncing (In development)
  Have one method, need to test with larger keyboard to verify performance.
HID enumeration as keyboard input device (Not yet started)
  USB controller known to be functional based on part manufacturer demo code for HID mouse enumeration.
Main keyboard Software

## Slide 47: Software Development Status
SPI display
  Minimally viable functionality complete
  Utilization and integration with remainder of system in development
sub-module Module Software

## Slide 48: Project Timeline

## Slide 49: 3D Printing
Questions?